## Slide 1: Implementation of a Total Power Radiometer in Software Defined Radios
Matthew E. Nelson
Iowa State University
Electrical and Computer Engineering

## Slide 2: Acknowledgements
POS Committee
Dr. Phillip Jones, Dr. Mani Mina, Dr. John Basart
Additional Support
Dr. Brian Hornbuckle
Special Thanks
My wife, Jennifer and my family for their support

## Slide 3: Table of Contents

## Slide 4: Introduction
The goal of this presentation is to present my research into implementing a total power radiometer using low cost hardware and software used in software defined radios.
This thesis looks to explore the following questions:
Can we use a SDR to recreate a radiometer in software?
If so, what performance can we get from the system?
Can we create a low cost SDR Radiometer that is effective?
What benefits do we obtain by using a SDR Radiometer?

## Slide 5: About the thesis
The goal of this thesis is to explore a low cost method for implementing a total power radiometer using a software defined radio and to demonstrate the effectiveness and benefits of this system.
Why a SDR?
A software defined radio infrastructure provides a highly flexible system that is able to adapt to different scenarios more quickly and at a lower cost than traditional radiometers

## Slide 6: Related Works
Radio Astronomy
Radiometers are used in a variety of remote sensing applications such as soil moisture and ocean salinity
Radio Astronomy is one method of using radiometers for remote sensing
There are current stations using Software Defined Radios for Radio Astronomy
Notes: Radiometers are used in remote sensing of soil, ocean and deep space. SMOS is an excellent example of a working soil and ocean measurement system.

## Slide 7: Related Works
The Shirleys Bay Radio Astronomy Consortium (SBRAC) located in Smiths Falls, Ontario is currently using a USRP software defined radio in conjunction with GNURadio
Notes: Marcus is the Principal Investigator at SBRAC and also a contributor to the radiometer branch in GNURadio. Although this branch is no longer maintained, he still answers questions about using radiometers with GNURadio SBRAC has successfully used this configuration to obtain radio astronomy data by looking at the hydrogen line at 1420.4058 MHz. The person in charge of this facility, Marcus Leech, contributed software to the GNURadio specifically for radio astronomy applications. It was this software branch that was used as the base for the GNURadio program that was used in this thesis.

## Slide 8: Related Works
Students at the University of Illinois and Grand Valley State University built a software defined radio to listen to emissions from Jupiter by building their own RF section and using GNURadio for the software. This software defined radio was built using an Analog Devices AD9460 and a Xilinx Spartan-3E-500 FPGA to build the SDR itself.
Notes: While the students in this paper built their own hardware, GNURadio was still used to develop the software. Another goal of this project was to produce a low cost solution using GNURadio.

## Slide 9: General Radiometer Theory
The primary goal of a radiometer is to measure power. While that statement sounds easy, there are in fact many factors that go in to how well a radiometer can measure the power it sees. In order to accurately measure power, we need to keep the following in mind.
Total System Noise
Bandwidth of the signal
Stability of the system
Notes: The primary goal of a radiometer is to measure power. While that statement sounds easy, there are in fact many factors that go in to how well a radiometer can measure the power it sees. A better statement would be that a radiometer’s primary goal is to accurately measure power within a certain degree of accuracy. In order to accurately and within a high degree of precision measure power, a radiometer must take into account various factors such as the system noise, the bandwidth of the signal and the stability of the system as a whole.

## Slide 10: General Radiometer Theory
A very simple and ideal radiometer is an antenna that amplifies a signal with a gain of G and is within a bandwidth of B or β. A device then measures the power from this system. The total power received by the is the noise temperature of the object it is pointed at. Therefore the brightness temperature of the source can be related to the brightness temperature at the antenna. We will refer to this brightness temperature as TA
Notes: To measure power we begin with the noise signal coming from the antenna. Our antenna is assumed to be looking at our target of interest and it is assumed that we can relate the antenna noise to the noise from the source. It is often easier to refer to this noise as the brightness temperature. Therefore the brightness temperature of the source can be related to the brightness temperature at the antenna. We will refer to this brightness temperature as TA

## Slide 11: General Radiometer Theory
A more realistic model is a system that includes the noise that is generated by the radiometer itself. This noise is added to the noise from the antenna.
Notes: The antenna itself also adds noise. Our greatest contributor to noise is from the LNAs. However mismatches in the RF chain and other factors can also increase this noise. This noise covers up or obscures the noise that we are interested in so we want to keep this to a minimum.

## Slide 12: RF Front End Design
The RF front end is one of the most critical components in a radiometer, both traditional and in our software defined radio setup. Although we have moved many components to be emulated in software, one component, the Low Noise Amplifier (LNA) can not be emulated in software. LNAs amplify our signal to increase our sensitivity while keeping as low as possible the noise it contributes to the system.

## Slide 13: Software Defined Radio
A software defined radio (SDR) is designed to mimic radio functions in software instead of using dedicated hardware. A radiometer is a radio that can detect changes in power. Therefore the SDR needs to be able to measure power coming from the source that we are looking at.
Notes: Software defined radios have been used in a number of applications, but usually related to communication systems. Changes to modulation and encoding/decoding is very easy for a SDR and this is why SDRs have grown in recent years. Use in remote sensing applications, as far as I know, is a relatively new application of SDRs.

## Slide 14: Software Defined Radio
To build a radiometer in software, we need to know what components are key to the radiometer and build them in software. There are four key components we can build in software.
Filter to the bandwidth we desire
Total power measurement
Integration
Record the data
Notes: Filtering can be done by limiting the sampling rate of the SDR, but we can also add additional filtering if desired.

## Slide 15: Software Defined Radio
Total power measurements is accomplished by squaring the phase and magnitude information provided by the SDR. Integration is a simple mathematical operation on the signal Recording the data is also trivial for the software to accomplish
Notes: The block shown is the TPR block we used in GNURadio. This combines the total power measurement and integration and low-pass filter into one block that we can call in other programs.

## Slide 16: Comparison
Traditional Radiometer
A traditional radiometer uses Low Noise Amplifiers, hardware based filters and a square-law detector to measure the total power received.
SDR Radiometer
A software defined radiometer eliminates the filters and the square-law detector and replaces this with their mathematical equivalents that is emulated in software.
Notes: SDRs can filter in two ways. First, by limiting the sampling rate we effectively put a bandwidth filter on the system. Two, we can also filter by constructing a filter in software, although there is some cost with this option in terms of CPU and memory requirements on the system

## Slide 17: Comparison
Traditional Radiometer
Most total power radiometers do not retain any frequency information, this information is lost and in most cases can not be recovered.
SDR Radiometer
Since we have both magnitude and phase information we can recreate the signal or manipulate it as needed. This allows for more in-depth analysis such as RFI mitigation.
Notes: SDRs give us a lot more information to work with. At the core of a radiometer, this information is not needed which is why it was often discarded. However, several papers have now been written that bring to light the need for additional information in order to deal with known issues with radiometers such as interference or new methods for determining total power such as the Stokes method. A key thing with a SDR radiometer is that in many ways it flexible enough to handle any future methods with either very little or no change in hardware.

## Slide 18: Implementation
A total power radiometer in software requires us to extract the magnitude (or amplitude) information from the I/Q data captured. This is equivalent to what a square-law detector does in determining the power measured.
Notes: Unlike an analog radiometer, the magnitude information is there and a simple squaring gives us total power. A square-law detector however has to do just that, it detects the power and then extracts that as a voltage.

## Slide 19: Implementation
For the SDR, the incoming signal is sampled and converted to I/Q values. The I/Q values represent the amplitude and phase information of the signal. In GNURadio we are then able to square these values within software. This block in GNURadio mathematically performs the following:

## Slide 20: Filtering
Filtering requirements in a software defined radio is different from a hardware based or traditional radiometer.
The bandwidth setting of the SDR only samples data within that bandwidth
Additional filters can be added at a cost of additional processing requirements
Because filtering is software driven, filters can be added or removed with no additional hardware required.

## Slide 21: Integration
The data we get from these power measurements fluctuate very quickly. We want to smooth out or filter this data by integrating this over time. In a traditional radiometer a hardware integrator is often used. In software, we can use an Infinite Impulse Response (IIR) filter as an integrator.